## Slide 1: Fusion Energy Research at LBNL
Fusion Power Associates Annual Meeting
Washington, DC December 5, 2018
PETER SEIDL, LBNL
Notes: Add slide for computing

## Slide 2: Our strategies and expectations through the 2020s
LBNL is well positioned to lead and make significant contributions to:
Intense ion beams for all approaches and applications to fusion.
HEDP and discovery science with laser generated intense ion pulses.
Advanced modeling and high-performance computing.
Applicable to plasma and particle beam modeling in general (laser-ion acceleration, plasma mirrors, …)
Magnetic vortex acceleration laser-ion pulse
State-of-art RF, induction & new compact accelerators
Notes: Conventional RF and also induction accelerators, where we made significant progress in developing high intensity ion beams for heavy ion driven inertial fusion energy. Also in the past fe years we have leveraged that to develop a new type of compact particle accelerator – more on that later.

## Slide 3: LBNL is advancing these topics for fusion energy sciences
High intensity laser-generated ion beams with Bella-i for materials research and HEDP via LaserNet US.
MEMS-based accelerators for materials testing and plasma heating (Cornell)
High-Tc magnets for high-field tokamaks, Berkeley Center for Magnet Technology BCMT.LBL.GOV (U. Houston, Tufts, Advanced Conductor Technologies)
Advanced simulations and computing for fusion research
Irradiation of semiconductor devices with pulsed ion beams at NDCX-II (LLNL, SNL, TU-Darmstadt)
2 mm
Notes: SUPERCON research: Majority HEP, but leveraged for FES.
NDCX: mention here that we continue to make use of it in a variety of areas, including rad effects testing of semiconductor devices and for biology.
LaserNet US: program was in response to a report that was issued by the National Academy of Sciences about a year ago, which assessed the United States’ position in laser science.
“The determination of the study was essentially that the U.S. has lost its lead to Europe, so LaserNet U.S. was established as a way to respond to that report and hopefully bolster high intensity research in the U.S.,” Ditmire said.

## Slide 4: 1. BELLA-i can have a transformative impact in High Energy Density Physics due to the 1 Hz rep rate and superb laser quality
(ultra)-relativistic plasma science at 1 Hz
fundamentals of laser ion acceleration
laser based ion beams and neutron pulses as a tool for discovery plasma science and applications
part of the new LaserNetUS
FES support to install a short focal length beamline to reach higher intensity.
Q. Ji S. Bulanov S. Steinke
J. Bin J. Park
Notes: No new data - but did extended data analysis, articles in preparation
Will make Bella available under LaserNet US (Kramer Akli DOE) .following on the recommendations of the NAS Report
Doing compressor scan to vary pulse duration and to seek the optimal pulse duration for ion energy.
Fusion relevant materials science
No new data
Will make Bella available under LaserNet US (Kramer Akli DOE) .following on the recommendations of the NAS Report
Doing compressor scan to vary pulse duration and to seek the optimal pulse duration for ion energy.
Fusion relevant materials science
LaserNet US: program was in response to a report that was issued by the National Academy of Sciences about a year ago, which assessed the United States’ position in laser science.
“The determination of the study was essentially that the U.S. has lost its lead to Europe, so LaserNet U.S. was established as a way to respond to that report and hopefully bolster high intensity research in the U.S.,” Ditmire.

## Slide 5: We have commenced ion acceleration experiments at BELLA-i
1um Ti
5um Ti
0.8 PW
Charge states up to Ti11+, C5+, O6+
5 shots averaged
Ti tape drive target for extended 1 Hz operation
Low ion pulse divergence, high ion number, publication in preparation, S. Steinke, Q. Ji, J. Bin, S. Bulanov, and BELLA team
Thomson parabola

## Slide 6: Transport of 1012 ions at 5-10 MeV to EMP-free environment possible with plasma lens
Active plasma lens to focus an ion beam to a 500µm spot 1m downstream of plasma lens:
Charge distribution at WDM target:
0.5mm
0.5mm
0.5mm
discharge current:
1012 ions in
3ns, 0.25mm2
van Tilborg et al., PRL 184802 (2015);
HYDRA, Temperature

## Slide 7: Short focal length, high Intensity beam line with double plasma mirror for dedicated HEDLP science
Double Plasma Mirror based on OSU liquid crystal technology
Poole et al., DOI: 10.1038/srep32041
Ex. long focal length beam line (f/60)
Re-collimating off-axis parabolic mirror
Final focus OAP (f/2)
Dedicated target chamber for HEDLP
8m expansion space, e.g., for ion beam line
Thomson spectrometer
New short focal length laser beam line for LaserNetUS experiments at >1021 W/cm2
High repetition rate Double Plasma Mirror will improve laser contrast by >104
(New equipment in yellow)

## Slide 8: 2. In the first two years we have developed the first MEMS based multi-beam accelerator
A. Persaud, Q. Ji, E. Feinberg, P. A. Seidl, W. L. Waldron, T. Schenkel, A. Lal, K. B. Vinayakumar, S. Ardanuc, D. A. Hammer, Rev. Sci. Instr. 88, 063304 (2017), http://dx.doi.org/10.1063/1.4984969, cover, June 2017
10 cm
Funded by the ARPA-e alpha program

## Slide 9: More recently, ion acceleration of 2.6 kV/gap and have accelerated ions in a 3x3 beam array to 3x the injection energy
P. Seidl, et al., https://arxiv.org/abs/1809.08525

## Slide 10: Electrostatic quadrupoles focus the ion beams for efficient transport in both PC board and silicon
laser cut PC board Silicon wafer
ESQ field distribution
3x3 array of quads, pitch = 5 mm
K. B. Vinayakumar, et al., IEEE, MEMS 2018, Belfast, Jan. 2018, arXiv:1802.02622
Notes: Silicon ESQ structure using DRIE process

## Slide 11: Outlook: build a 300 keV compact accelerator
We now operate a multi-beam accelerator formed from a stack of PC boards
Next step is scaling to higher beam current (from 50 µA to >1 mA) and higher beam energy (10 keV to >100 keV)
This will be highly competitive/disruptive for mass spectrometry, neutron-generators, surface treatment, ion implantation, plasma diagnostics, …
Later, scaling to ~1 MeV/m and >1 A for plasma heating
  e.g., Neutral beam injectors for MFE, where electrostatic MV holdoff is challenging.
1:1 model of a 300 keV accelerator for argon ions at 20 MHz
50 cm

## Slide 12: 3. LBNL is a leading magnet lab for HEP. HTS for high field tokamaks: quench protection, electromechanical performance, and feedback to industrial manufacturers. S. Prestemon, LBNL
Tapes  fusion scale cables: A curvature-based method for cable and magnet designs based on CORC® cable &stacked tapes
, X. Wang et al., IEEE Trans. Appl. Supercond., https://doi.org/10.1109/TASC.2017.2766132
F. Pierro et al, presentation at MT25, September 2017, https://indico.cern.ch/event/445667/contributions/2564508/
Instrumented U-spring sample holder made of Aluminum-Bronze
First results on the Ic-strain dependence on the latest 2-mm wide, 30 μm thick substrate commercial REBCO samples.
Observed 8% reduction in Ic with 0.46% tensile strain (data shown is reversible)
Characterize the electro-mechanical performance of REBCO conductors
Collaborate with the community to characterize the transport performance of advanced REBCO tapes and cable prototypes
Wire Je ~ 300 A/mm2 at 15 T, 4.2 K
Leverage the HEP programs to develop and evaluate advanced concepts for quench detection
M. Marchevsky et al.,EUCAS, 2017
M. Marchevsky S. A. Gourlay, doi:10.1063/1.4973466
Thermo-acoustic quench detection
Bending<-> performance

## Slide 13: 4. Advanced modeling and computing: Toward Plasma Physics Simulations at Exascale. J. L. Vay LBNL
New code WarpX part of U.S. DOE Exascale program
Goal is to develop code modeling 10s-1000s stages for 1-30 TeV plasma collider by ~2030
LBNL+SLAC+LLNL multidisciplinary team of physicists, applied mathematicians & computer scientist
Implement best algorithms on latest hardware (manycore, GPUs, …)
Boosted frame
AMR
Spectral solvers
Galilean solver
…
Program is on track with first 3D MR simulations of plasma accelerators
100 MeV stage 9/2017
Multi-GeV stage with MR by 9/2018.
WarpX released open source 10/2018
Available via Berkeley Lab Accelerator Simulation Toolkit (blast.lbl.gov)
Applicable to plasma modeling in general (laser-ion acceleration, plasma mirrors, …)
PI: JL Vay
MVA laser-ion acceleration

## Slide 14: LBNL is advancing these topics for fusion energy sciences
High intensity laser-generated ion beams with Bella-i for materials research and HEDP via LaserNet US.
MEMS-based accelerators for plasma heating & materials testing (Cornell)
High-Tc magnets for high-field tokamaks, Berkeley Center for Magnet Technology BCMT.LBL.GOV (U. Houston, Tufts, Advanced Conductor Technologies)
Advanced simulations and computing for fusion research
Irradiation of semiconductor devices with pulsed ion beams at NDCX-II (LLNL, SNL, TU-Darmstadt)
2 mm
Notes: SUPERCON research: Majority HEP, but leveraged for FES.
NDCX: mention here that we continue to make use of it in a variety of areas, including rad effects testing of semiconductor devices and for biology.
LaserNet US: program was in response to a report that was issued by the National Academy of Sciences about a year ago, which assessed the United States’ position in laser science.
The U.S. was the dominant innovator and user of high-intensity laser technology in the 1990s, but now Europe and Asia have taken the lead, according to a recent report from the National Academies of Sciences, Engineering and Medicine titled "Opportunities in Intense Ultrafast Lasers: Reaching for the Brightest Light."
Currently, 80-90 percent of the world's high-intensity ultrafast laser systems are overseas, and all of the highest power research lasers currently in construction or already built are also overseas. The report's authors recommended establishing a national network of laser facilities to emulate successful efforts in Europe.
LaserNetUS was established for exactly that purpose. The network will hold a nationwide call for proposals for access to its facilities, and the proposals will be peer reviewed by an independent panel. This call will allow any researcher in the U.S. to get time on one of the high intensity lasers at the LaserNetUS host institutions.
The LaserNetUS institutions are U-M, University of Texas, Ohio State University, Colorado State University, University of Nebraska, University of Rochester, SLAC National Accelerator Laboratory, Lawrence Berkeley National Laboratory and Lawrence Livermore National Laboratory. The funding comes from the DOE's Fusion Energy Sciences program within the Office of Science.

## Slide 15: Our team
J. Bin, S. Bulanov, Q. Ji, M. Marchevsky, W. Mixter*, J. Park, A. Persaud, S. Prestemon, D. Raftrey*, W.L. Waldron, P. Seidl, S. Steinke, J.L. Vay, G. Woods*, T. Schenkel, LBNL
D. Ni, K. Vinayakumar, A. Lal, Cornell University J.J. Barnard, A. Friedman, D.P. Grote, LLNL D. Di Domenico*, D. Oberson, School of Engineering and Architecture, Fribourg, Switzerland
F. Treffert*, TU Darmstadt, Germany (now @ SLAC)
E. B. Bielejec, B. Vaandrager, Sandia Nat Lab.
Univ. of Houston. Tufts Univ.
*5 students
Notes: We typically have about 5 students/year, including some undergrads from the DOE sponsored SULI program.

## Slide 16: Thank you!

## Slide 17: WarpX dynamic local balancing speeds up 3-D simulation of Magnetic Vortex Acceleration ion acceleration scheme
accelerated
ions
Toroidal B field lines
Mesh refinement (static or adaptive) expected to bring additional speedups.
Simulations and visualization by Jaehong Park, in support of BELLA-i, LBNL.

## Slide 18: We are operating with long focal length and will now implement a short focal length beamline with a dedicated target chamber for HEDLP in LaserNetUS
f\2.5
f\65
in operation now, 2x1019 W/cm2 , large laser spot, 100 m, low divergence ion pulses with 1012 protons
one time ask of $2M, >1021 W/cm2, small laser spot, ~10 m, (ultra)-relativistic plasma science at 1 Hz, advanced ion acceleration, high energy ions (>100 MeV)
Notes: low divergence <250 mrad (14 degrees)

## Slide 19
Intense, short ion pulses for materials studies and fusion science
Lower intensities:
defect dynamics in materials
 fusion materials
isolated
cascades
overlapping
cascades
amorphization
and melting
warm (~1 eV),
dense matter
1-30 nC, 0.3 -1.2 MeV, few mm2, ~1-30 ns
Higher intensities:
extreme chemistry and warm dense matter
NDCX --- Bella-i
Notes: Understanding the multi-scale dynamics of radiation induced defects is of fundamental interest. It is important to benchmark simulations codes of dynamics, but there is little data on short timescales. Application: Engineer fusion materials for the burning plasmas and IFE.

## Slide 20: NDCX and Bella-i advance intense beams, beam-plasma physics, materials, warm dense matter science
At NDCX, we have generated ns ion pulses with peak dose rates of >1020 ions/cm2/s with high reproducibility. Repetition rate is <1/minute. Beam r = 1mm, t = 2 ns
We have achieved 2 A peak currents for ns pulses of 1 MeV He+ ions, focused to 0.1 J/cm2.
We are measuring ion energy loss in heated foils
  Radiation effects on semiconductor transistors.
2 mm
NDCX He+ beam
Synergy: NDCX & Bella-i laser generated ion beams:
250 mrad
Bella-i
Notes: The goal of this workshop is to discuss opportunities to understand and steer the dynamics of radiation effects in situ using emerging pump-probe techniques.
Topic Areas:
Theory and simulations of the dynamics of radiation effects in materials;
Excitation sources such as pulsed plasmas and pulsed ion beams paired with in situ probes such as Ultrafast Electron Diffraction, pulsed x-rays, optical and ion scattering techniques
Application Areas:
Materials for high radiation environments for fission and future fusion reactors, radiation effects on electronics, phase transitions and materials synthesis far from equilibrium

## Slide 21: 1. NDCX: Exploring the dynamics of the disruptions due to rapid heating using the 3D multi-physics, multi-material code ALE-AMR*
Opportunity to understand materials dynamics through a solid-liquid phase transition with rapid, uniform heating.
  Work in progress, adding surface tension model to the simulation
*LIU, KONIGES, GOTT, et. al, Computers and Fluids (2017)
…with impurity
Pure Sn foil
preliminary
1 mm

## Slide 22: NDCX: Radiation Effects Studies with Intense Pulses of Helium Ions on transistors
We have explored the effects of high ion flux, short pulse irradiation on the Messenger-Spratt damage factor using Microsemi 2N2907 pnp transistors.
We have applied an ion flux of 1018 – 1019 ions/cm2/s per ~10 ns long helium ion pulse (1 MeV).
We have measured late-time gain degradation as a function of ion fluence for a series of shots up to 2.5x1011 ions/cm2.
Ion pulses simulate pulsed neutron irradiation*.
NDCX delivers dose equivalent 104X n/cm2/s vs IBL @ SNL.
End-of-range ion energy loss at the base-emitter junction, where damage leads to gain degradation.
* Aguirre, et al., IEEE Trans. Nucl. Sci. (2017)
Example of a measured Messenger-Spratt curve to determine the damage constant
E. Bielecek, SNL
Schenkel, et al., J. Rad. Effects, Res. Eng. (2017)
Ludewigt, et al., JRERE, submitted (2017)
Funded by NNSA via SNL
Notes: 1e4 (NDCX) and 1e5 (Bella-I, future) equivalent n/cm2/s dose rate over …
See dose rate effects @ 10^11 ions/cm2/shot -- check

## Slide 23: We envision that the compact RF accelerators fit in the footprint of the DEMO NBI system
Nucl. Fusion 57 (2017) 056026 P. Sonato et al.
modular: 2x10 RF sources and injectors

## Slide 24: Assume 60 Amps total current, 1 MeV D-, 3 NBI ports on tokamak. Each NBI has:
46 accelerators, two rows per injector system
Accelerator components:
  6-inch square wafers, 2 cm border on wafer.
  1080 beamlets/wafer, total current 0.43 A.
Room for pumping/conductance
  4 cm gap between accelerators
Accelerators can be angled to achieve overall convergence to match port area at tokamak wall
Assume injector J = 20 mA/cm2
  Beam-beam pitch = 3 mm
  2x margin for losses: Plasma source aperture dia = 1 mm, inject 0.62 mA/beamlet (@ 20 mA/cm2), but need 0.32 mA/beamlet

## Slide 25: Accelerator array for NBI system is a converging group of beams injected into neutralization system. 1 MeV, 20 A
2 rows, 23 accel/row
Neutralization
section
4.5 m
2-4 m
Residual ion dump
Neutron-dump
3.5 m

## Slide 26: Accelerator array for NBI system is a converging group of beams injected into neutralization system. 1 MeV, 20 A
2 rows, 23 accelerators/row
neutralization
RID
N-dump
Tokamak beam port

## Slide 27: NDCX and Bella-i advance intense beams, beam-plasma physics, materials, warm dense matter science
We have generated ns ion pulses with peak dose rates of >1020 ions/cm2/s with high reproducibility. Repetition rate is <1/minute. Beam r = 1mm, t = 2 ns
We have achieved 2 A peak currents for ns pulses of 1 MeV He+ ions, focused to 0.1 J/cm2.
We are measuring ion energy loss in heated foils
Based on new results, we will:
  Push the limits and testing the understanding of intense beam physics for inertial fusion and other applications.
  Dynamics of radiation effects and fusion materials science
  Radiation effects on semiconductor transistors.
Workshop on Dynamics of Radiation Effects, Dec 15-16, 2016, Berkeley Lab
  Theory and simulations of the dynamics of radiation effects in materials;
  Excitation sources such as pulsed plasmas and pulsed ion beams paired with in situ probes such as Ultrafast Electron Diffraction, pulsed x-rays, optical and ion scattering techniques
Synergistic: Bella-i laser generated ion beams
2 mm
Notes: The goal of this workshop is to discuss opportunities to understand and steer the dynamics of radiation effects in situ using emerging pump-probe techniques.
Topic Areas:
Theory and simulations of the dynamics of radiation effects in materials;
Excitation sources such as pulsed plasmas and pulsed ion beams paired with in situ probes such as Ultrafast Electron Diffraction, pulsed x-rays, optical and ion scattering techniques
Application Areas:
Materials for high radiation environments for fission and future fusion reactors, radiation effects on electronics, phase transitions and materials synthesis far from equilibrium

## Slide 28: First commissioning shots show narrow divergence beams at expected ion energies
2 cm
12J on target, 5x1018 Wcm-2
13um Aluminum
Ion energies up to 4.5 MeV
Divergence (FWHM) 150mrad
Experiment Parameters
1 MeV
4.7 MeV
250 mrad
250 mrad
RCF film stack
13um Al target

## Slide 29
beam spots size with radius r < 1 mm within 2 ns FWHM and approximately 1010 ions/pulse.
0.02 A  0.1 mA  0.6 A.
The NDCX-II induction accelerator compresses beam to ns and mm bunches on target.
Ion source and injector, 500ns
Target
Linac custom waveforms for rapid beam compression
Neutralized drift compression and final focus
Z=10 m
P.A. Seidl, et al., NIM A800 (2015)
For I >10 A: Q=2qI/(4peoMv3) ~ 10-2
Unique opportunity to study intense beam and beam plasma physics.
Stepanov, et al., “Optimizing Rapidly Compressing Beams…” MRE (2017) submitted.
Extensive integration of PIC simulations: Snapshot of the X-Z projection shows rms properties & halo particle loss…
Applied accel and bunching V(t) from database
Notes: NDCX beam is characterized by high perveance and low emittance, which lends itself to studies of the beam physics questions raised here.
Velocity increase ~2.7x from 165 kV to 1.2 MeV
Current increase 5x
Bunch compression (length or lambda) = 5/2.7 = 1.8
All components of the Neutralized Drift Compression Experiment-II (NDCX-II) have been integrated and commissioned. The first results demonstrate the generation of intense nanosecond ion pulses with reproducible peak dose rates of 10^20 ions/cm /s.

## Slide 30: With a Thomson Parabola spectrometer we measure the transmitted particle energy distribution and species identification
1.1 MeV He+, no target
E field deflection 
 B field deflection
He+
1.1 MeV He+ on 1 mm Si
F. Treffert, TU-D, Masters thesis
1.1 MeV He+ on 1 mm SiN
DE ≈ 0.54 MeV
0o (channeling)
DE ≈ 0.32 MeV
Pixel resolution ∂E ≈10 keV
Exploring intensity and dose rate effects
He2+

## Slide 31: Scintillator luminescence shows dose effect from intense helium ion bunches
Fast CCD camera
Streak camera
Focused and defocused beam to explore dose rate effect.
Lifetime loss from increased temperature (DT ≈ 60 C).
Bond breaking (C-H)  color centers decrease transparency.
Thermal annealing of color centers, restoring transparency.
Zimmer, et al, “Dose rate effects ... PVT”, in preparation
t
l
polyvinyltoluene (PVT)
105 Gy/shot
Notes: Temp effects dominant in center of beam profile. ∂T ≈ 60 deg
Intermediate region, thermal annealing of color centers, which helps to
PVT based scintillators are experiencing quenching effects in the scintillation light yield for stopping powers higher than 2.5keV/μm as a result of non-radiative de-excitations4 from single ions that create local accumulations of excited molecules.

## Slide 32: Helium pulses with 100 mJ/cm2/shot @ edge of tin melting plateau
J. Barnard
0.5 mm Sn experiment
Notes: This is a mathematica script, that includes the specific heat of tin, the heat of fusion (melt) of tin,
and uses the range of He in tin (as a function of energy) obtained from SRIM. It's just a few lines.
This is the basic equation in Mathematica:
kT = Which[energydensityperatom < energytomeltingtemp,
kT0 + energydensityperatom/specificheat,
energydensityperatom > energytomeltingtemp && energydensityperatom < energytomeltingtemp + latentheatofmelt,
meltingtemp,
energydensityperatom > energytomeltingtemp + latentheatofmelt,
meltingtemp + (energydensityperatom - energytomeltingtemp - latentheatofmelt)/specificheat];
Here,
energytomeltingtemp = specificheat*(meltingtemp - kT0);
energydensityperatom = energydensitypergram*targetmass*amumass*10^3/qcharge; (* eV *)
energydensitypergram = depositedenergyfraction*fluence/(rhotarget*foilthickness);
(All the energies and temperatures above are expressed in eV). (Deposited energy fraction is obtained from SRIM).

## Slide 33: Heating 0.3-mm foil Tin with a short-pulse helium beam
Fast Faraday cup
Q = 4 nC, 6 ns FWHM
  1 mm
Peak fluence: 0.035 – 0.045 J/cm2
E = 0.8 MeV
Scintillator image
Foil under microscope
Notes: Note: Warp run with input voltages and timing suggest 1.0 MeV. TOF gives 0.8 MeV. Check.

## Slide 34: Inspection of 0.5 mm Sn foil after Qtot = 12-nC/beam pulse
#1
2
3
4
5
6
#7
1 shot/target position >1 shot/target position
Backlight view shows tiny holes
2 mm
1 mm

## Slide 35: We measure the energy loss of transmitted ions in heated targets via TOF, Thomson Parabola spectrometer
12 nC
He+
scintillator
0.5 mm Sn
FC-t
FC-d
Exploring dose rate dependence
Opportunity to probe material response to short-pulse ionizing radiation (t, l), e.g., channeling of ions in crystals

## Slide 36: We welcome visitors and collaborations!
We are doing target experiments with >10 nC/pulse, 2-40 ns, r ≈ 1mm, >1/minute.
We have developed a close coupling of particle-in-cell modeling to the experiment.
These intense pulsed ion beams now open opportunities in the materials physics of radiation with in situ access to multi-scale defect dynamics, radiation effects in semiconductors, intense beam and bam-plasma physics
Synergistic: Bella-i laser generated ion beams

## Slide 37: LBNL is advancing these topics for fusion energy sciences
High dose-rate irradiation of materials with pulsed ion beams at NDCX-II (LLNL, SNL, TU-Darmstadt)
High intensity laser-generated ion beams with Bella-i for materials research and warm, dense matter / HEDP
MEMS-based accelerators for plasma heating (Cornell)
High Tc superconducting magnets for high-field tokamaks (U. Houston, Tufts, Advanced Conductor Technologies)
Advanced simulations and computing for fusion research
2 mm

## Slide 38: We have achieved 2 A peak currents for ns pulses of 1 MeV He+ ions
1.1 MeV (He+), 12 nC (7.5x1010 ions)  13 mJ
~180 mJ/cm2 @ peak, 2 mm FWHM
Uniform energy deposition into a 2 micron silicon foil with ~ 6x103 J/cm3
Highest fluence achieved 0.7 J/cm2 for longer pulse duration.

## Slide 39: Diagnostics include fiber-coupled streak spectrometer, II-CCD, Fast detectors for TOF, channeling and energy loss experiments.
Target chamber available diagnostics:
  Scintillator + CCD camera, Fast Faraday cup (FFC)
  Streaked optical spectrometry (10 ps)
Induction Core
Ferro-Electric Plasma Source Cathodic Arc Plasma Source Light Collection system Beam Position Monitor accel. Gap
20 ms movie
of FEPS plasma
Scintillator beam image for solenoid tuning
B= 8 T
  New: Thomson parabola
Notes: Diagnosis to short timescales not limited by the ns bunch duration, for example as with transient decrease in the transmission of channeled ions
The peak near 400 nm is attributed to a convolution of the broad emission peak due to the d 􏰛f transition in Ce3+ [22] with the wavelength cut-off of the optical fiber at 400 nm. Separately, analysing the emission near 400 and 440 nm we find exponential decay constants of 30 and 24 ns, respectively, similar to photon luminescence results for YAP [22, 23, 24]. This structure will be explored in future experiments in relation to earlier observations of excitation specific emission structures from luminescent materials [25].

## Slide 40: Routinely use particle-in-cell simulations to to validate our understanding of the high intensity beam physics and to help optimize the performance of the accelerator, compression and focusing for target experiments.
1. Beginning with model of plasma ion (He+) source injection, the experiment voltage waveforms are imported from DAQ database & applied to the 2D Warp simulated beam… 
-- V(t) from database
-- Warp modeled beam
3. Results are directly compared to the experiment beam  diagnostics. From these, adjust focusing, waveforms, timing, then go to #1.
-- Experiment diagnostic
-- Warp modeled beam
2. Snapshot of the X-Z projection shows rms properties & halo particle loss… 
Applied accel and bunching V(t) from database
≈10 min/run/processor, we do ≈10 parralel simulations, vs 1 shot/min in the experiment
Notes: Beam potential at end of accelerator and before neutralization is ≈ 1-2 kV

## Slide 41: To determine the kinetic energy distribution for each shot, we have simulated each shot with Warp PIC.
Low energy ions do not reach the sensitive layer.
Analysis will separate range effects from possible dose rate effects.
E = 1.07 MeV
E = 0.90 MeV

## Slide 42: Opportunity to probe material response to short-pulse ionizing radiation (t, l), e.g., channeling of ions in crystals
T. Schenkel et al., Towards pump–probe experiments of defect dynamics with short ion beam pulses, NIM B 315 (2013)
Beam
Target
Faraday Cup
α
Time [µs]
1 µm target E0=287 keV
F-cup
+ target
F-cup only
x 0.1
Li 135 keV Si 250 nm
Current [mA]
Current [mA]
Aperture
Rotation, α [degree]
current
Loss due to
damage
build-up
time
Notes: Access to time domain.
A non-channeling ion hitting the material will create many interstitial-vacancy pairs in the material, temporarily blocking many channels in the material before the defects self-anneal. If the fluence of the ions is high enough, other ions will hit the same area as the remnants of the earlier ion cascade (before the self- annealing took place) and the channel transmission will be impeded. Therefore, we expect that the channeling current will change depending on the fluence, e.g., for low fluences channeling will be unobstructed (no over- lapping cascades) and for high fluences the channeling current will decrease during a single beam pulse (many overlapping cascades). The transmitted beam current can be monitored with high temporal resolution and by restricting the measured ions to a small scattering angle, mostly channeled ions can be recorded. Noise from non- channeled ions can be further reduced by time-of-flight measurement, since channeled ions will have a smaller energy loss than scattered ions.

## Slide 43: The neutralization of the beam space charge defocusing is essential for obtaining higher focused intensity
plasma
no plasma

## Slide 44: With pulsed ion beams we can probe the radiation effects on materials and warm dense matter research
Novel opportunities with short, intense pulses to probe material response to radiation in the time domain.
e.g., single shot ionoluminescence of YAP:Ce measured with a streaked optical spectrometer.
P.A. Seidl, et al., NIM A800 (2015)
Helium beam on 0.75 m thick gold target
(Hydra), J. Barnard, LLNL.
Max pressure
at 0.6 ns
Notes: The peak near 400 nm is attributed to a convolution of the broad emission peak due to the d 􏰛f transition in Ce3+ [22] with the wavelength cut-off of the optical fiber at 400 nm. Separately, analysing the emission near 400 and 440 nm we find exponential decay constants of 30 and 24 ns, respectively, similar to photon luminescence results for YAP [22, 23, 24]. This structure will be explored in future experiments in relation to earlier observations of excitation specific emission structures from luminescent materials [25].
Hydra: radiation transport and hydrodynamics, atomic physics, lagrangian mesh
Right:
It does show differences in EOS, but might say that the temperature is optimistic, since our fluences will be lower than what was simulated.

## Slide 45: Strong collective focusing of an ion beam in a plasma and a weak magnetic field
Most pronounced when the beam radius is small compared to the collisionless plasma electron skin depth rb < c/wpe
Applied B can be reduced by a factor (me/mi)1/2 ~10 Tesla ~102 Gauss
Can this be used to great advantage in high intensity ion beams?
Particle-in-cell (LSP) simulation using the collective focusing effect to focus the high intensity beam using a weak magnetic field and a plasma.
Dorf, Davidson, Kaganovich, Startsev, Phys. Plasmas (2012)
Notes: Maybe skip this one

## Slide 46
Complementary aspects of intense, pulsed ion beams from accelerators
 | Fair | NDCX-II (goal)
Ions/pulse (total) | ~1010 - 1012 | 1010 (3x1011)
Pulse length | 40-100 ns | 2 ns (~1 ns)
Typical spot size | ~1 mm2 | 1 mm2
Ion species | H, C, …, Au | He (also H and higher Z)
Ekin | 0.4 – 1 GeV/u | 0.12 - 1.2 MeV
Energy spread | low | ~10%
Repetition rate | fast | 2/min
Target temp. | few eV, to ~100 eV | <0.1 eV (~1 eV)
Radiation environment at the target | Intense, requires shielding | Benign, no shielding required
Heated volume | > mm3 | ~1 mm2 x 5µm =5x10-3 mm3

## Slide 47: Two-stream instability of an ion beam propagating in background plasma
In high energy accelerators: two-stream or electron cloud effects arise from stray (unwanted) electrons.  Reduce/eliminate!
For new high-intensity ion beam systems, plasma is introduced to cancel the defocusing space charge force.
Beam density contour at t = 100 ns (1 m propagation).
Tokluoglu, Kaganovich, PPPL, Phys. Plasmas (2015)
Beam density contour at t = 300 ns (3 m of propagation).
Z(cm)
Z(cm)
x(cm)
NDCX-II beam parameters
rb=1 mm.
Defocusing when Dv/v is small.
Goal: observe transverse defocusing and longitudinal self-bunching of beam
[Kaganovich, APS-DPP invited]

## Slide 48: Demonstrate removing a large velocity spread from a high space charge beam via drift compression. Reduces chromatic aberrations in the final focusing elements.
Waveform errors can launch space charge waves, and degrade the final energy spread and may cause particle loss. Detailed initial conditions must be included in simulations.
vz
z
~10x compression
Pulse shaping: pump-probe
for materials
studies
Li+
ideal
More realistic
How well can space charge “stagnate” the compression to produce a “mono-energetic” beam at the final focus?
J. W-K. Mark, et al.
simulated line-charge profile
Double pulsing @ NDCX-II
(preliminary)
Explore driver final pulse shaping
Callahan, Tabak, Phys Plasmas (2000)
Friedman et al, NIM A (2001)
Vz (107 m/s)
Exp connect to HIF parameters: Perveance, “tune depression,” compression ratio) ~ a fusion driver.
PIC sim w/ perturbation wave
Notes: First time for an intense ion beam?
We will commence with the ~1 us-long pulse, and explore the creation and compression of an even longer pulse with uniform charge distribution over most of its length.

## Slide 49: We can probe the materials physics of radiation damage in situ on short time scales with pulsed ion beams at NDCX-II
One intriguing possibility is the use of pulsed ion beams to enable a “pump” that could in principle be “probed” in the time scale of the modification. This tool could transform our understanding of ion induced damage in the context of the complex evolving, reconstituted materials under fusion reactor conditions. (P. 116)