## Slide 1: Fusion Power Associates 40TH ANNUAL MEETING
Dec.3-4,2019 Grand Hyatt Washington
Chief Fusioneer Satoshi Konishi
Fusion Energy: Perspectives and Planning

## Slide 2
Kyoto Fusioneering Ltd. was founded in 2019 to provide B2B technical assistance for fusion challengers.
Private Fusion Developers are physics driven.
However their investors expect clear and compelling demonstration
- How fusion makes money?
We can provide
-blanket
-reactor components
-fuel cycle
-BoP
-reactor engineering
-plant design
-economic assessment
-strategy planning…
What We will Provide
Fusion Power Associates 40th annual meeting 2019

## Slide 3
Carbon budget of post-Paris agreement age will run out after 2040, if majority of the countries would be honest.
Carbon Removal is more critical than fossil fuels.
While Clean electricity can be supplied various options,
very few Alternative Fuel are known.
Further, Carbon Isolation is more serious, precious
Resource for future...
Electricity may be sold, but cheap.
Grid Parity/Stability, Alternative Fuel, and
Ultimate Disposal of Carbon have stronger demands.
Fusion may provide a solution for this issue.
Fusion Market Perspectives
Fusion Power Associates 40th annual meeting 2019

## Slide 4
Carbon Budget (by IEA)
What we will run out is not fossil resource,but carbon budget.
“Negative Carbon” will be
Most precious energy resource beyond 2040.
Oil and coal canont be sold not because of high price, but High penalty.
Carbon budget of post-Paris agrll run out after 2040,
CCS resource is more critical than fossil fuels.
Fusion can provide alternative
CCS technology
Fusion Power Associates 40th annual meeting 2019

## Slide 5
California Independent
System OperatorCAISO)
Value of the electricity (even clean base load) can be negative.
→Fusion Electricity may not recover investments!
Value of the electricity (California duck)
In the deregulated market,
Price of electricity varies.
Due to large share of renewable,
electricity market price drops in
day time.
Fig. Change of electricity demand in a sunny day
Instability of grid (frequency
change and outage) is
Serious when share of
Renewable increased.
Fusion Power Associates 40th annual meeting 2019

## Slide 6
Stranded Assets
・Fossil resources become “stranded” because they cannot be sold
・Many of the large scale long terminvestment (bond)in the world, particularly pension fund is highly dependent on fossil assets
・Value of the fossil assets drops under low carbon economy
“Divestment” from carbon to technology is happening.
Fusion Power Associates 40th annual meeting 2019

## Slide 7
Chemistry of biomass conversion
cellulose：（C6H10O5）n/6+ n/6H2O → nH2 + nCO – 136n [kJ]
lignin: (CH1.4O0.3)n + 0.7nH2O → 1.4nH2 + nCO –136n[kJ]
Biomass
(1kg)
+
H2O
External Heat，900℃
H2,CO
2H2 + CO → -CH2- + H2O + 160 [kJ]
Fischer-Tropsch reaction
CO + H2O ⇔ H2 + CO2 + 32 [kJ]
Shift Reaction
hydrogen
Carbon Neutral
8.2MJ
15.6MJ
24.2MJ
16MJ
8.1MJ
Heat for generation
diesel(hydrocarbon)
Carbon free oil 0.5 liter
Biomass gasification
Fusion Power Associates 40th annual meeting 2019
Notes: こちらが、それぞれセルロース、リグニンの代表的な元素組成のCHO比から想定される水蒸気と反応した理想的なガス化を示す式です。
一方、このときに起こると考えられる代表的な平行反応には。これらの反応式が示すようにメタンを生成する反応や、一酸化炭素と水蒸気から水素と二酸化炭素を生成するシフト反応があります。簡略化のために炭素２個以上の反応は考慮していません。
こちらが本研究で用いる、パラメータである水素生成率、炭素分解率の定義式です。水素生成率は、全ての反応が理想的に上式で起こったときの水素生成量を100%とし、実際の生成量より求めます。炭素分解率は、バイオマスのもつ炭素原子数が一酸化炭素、二酸化炭素、メタンの炭素ガスにどれぐらい分解されたかを示します。
(0:55)

## Slide 8
・Carbon-free fuels required
Substitute fewer than electricity source
・Competition in electricity market is tough
・Future fuel use
－ Fuel cells , automobile
－ aircrafts, ships
・Grid parity/stability
Dispersed electricity system
－ Cogeneration
－ Fuel cell,
－ micro gas turbine
(could be other synthetic fuels)
  Why fuels?
Aircraft
Automobile
2100
0
5
10
15
20
25
2000
2020
2040
2060
2080
Year
Electricity
Solid Fuel
Liquid Fuel
Gaseous Fuel
Energy demand(GTOE)
Example of Outlook of Global Energy
Market 3 times larger than electricity
Fusion Power Associates 40th annual meeting 2019

## Slide 9
Fusion Energy Balance
◯Large energy gain Q (>20) needed for DEMO because of poor
generation efficiency.
Net plant energy output(fuel)
Driver
Energy
Pd
Fusion
Energy
Multiplication
fusion energy
Pd
Blanket
Output
Generation
Efficiency
η ~0.33
Conversion
Efficiency
η 2.0~2.7
○If fusion plant is used for fuel production, fusion energy is
fully converted to output, adding to chemical energy from
biomass.
required energy multiplication Q could be as low as 3!!
Fusion Power Associates 40th annual meeting 2019
Biomass
Chemical
energy
Q =

## Slide 10
Relaxed Lawson criterion and efficiency η
◯High Plasma Q not required
・Positive plant energy balance
・larger energy efficiency
Practical energy generation
Larger than electricity
18
10
10
22
10
21
10
20
10
19
1
10
100
ｎt
Ｔ（ｋｅｖ）
Break-even
Ｑ＝１，η＝１
Electricity
generation
Ｑ＝20，
ηe＝0.33
biofuel
Ｑ＝５，
ηｆ＝２．７
◯Low Q plasma can be competitive
・possible marketing as oil fuel
・earlier introduction
・easier plasma requirements
○smaller plant→
Ｑ＞５，Ｒ<5 m is sufficient!
Fusion Target is easier
By “Hybrid Effect”.
6
10
-0.6
Negative power
ITER
DEMO
Net plant energy output
Fusion Power Associates 40th annual meeting 2019

## Slide 11
FUSION
Local
Electricity
Gasification reactor
H2+CO
Liquid
Fuel
Grid
Electricity
Fuel Cell
Fischer Tropsch process
BIOMASS
“apparent”
energy multiplication
Fusion-Biomass energy flow
Start-up and
driving
Fuel Cell
Residential heat
Process heat
Fusion Power Associates 40th annual meeting 2019
Grid Stability

## Slide 12
Biomass Hybrid fusion plant
Liquid blanket
Rp=5.2m
Biomass:180t/h
Pn ~0.5MW/m2
IHX
cellulose：（C6H10O5）n/6+ n/6H2O
→ nH2 + nCO – 136n [kJ]
Pf 320MW
2H2 + CO → -CH2- + H2O + 160 [kJ]
Fischer-Tropsch reaction
Diesel:90kl/h
~760MW eq.
Fusion reactor smaller than ITER with same physics
Used for endo-thermic reaction for bio-fuel production
Energy output larger than pure fusion.
Fusion Power Associates 40th annual meeting 2019
Notes: We have proposed the Fusion-biomass hybrid reactor for fuel production.
The characteristic of this reactor are small major radius and neutron wall load.
In this concept, fusion power is used for biomass gasification for hydrogen or fuel production.
To achieve high efficiency of biomass gasification, high temperature extraction over 900 degree C is required.

## Slide 13
Cellulose/lignin：
(CH1.6O0.6)n = nC+0.4nH2+0.6n H2O-451n kJ
Biomass
C, H2O, H2
Hydrogen fuel
1 GW electricity equivalent
2.5Mt/ycarbon=9.3MtCO2/y
Emission reduction credit
450M$/y assuming 50$/tonCO2
Charcoal
CO2
photosynthesis
Solar energy
Carbon stored as solid charcoal at ambient temperature and pressure
Fusion
3GW heat
440M$/y assuming
5 cent/kwh
Carbon negative energy system
Fusion Power Associates 40th annual meeting 2019
→Fusion has unlimited market chance of “negative carbon” by abundant energy.
100,000 unit-operation year of 3GW fusion plant market.(7.4 TtonCO2 to solidify)
Notes: こちらが、それぞれセルロース、リグニンの代表的な元素組成のCHO比から想定される水蒸気と反応した理想的なガス化を示す式です。
一方、このときに起こると考えられる代表的な平行反応には。これらの反応式が示すようにメタンを生成する反応や、一酸化炭素と水蒸気から水素と二酸化炭素を生成するシフト反応があります。簡略化のために炭素２個以上の反応は考慮していません。
こちらが本研究で用いる、パラメータである水素生成率、炭素分解率の定義式です。水素生成率は、全ての反応が理想的に上式で起こったときの水素生成量を100%とし、実際の生成量より求めます。炭素分解率は、バイオマスのもつ炭素原子数が一酸化炭素、二酸化炭素、メタンの炭素ガスにどれぐらい分解されたかを示します。
(0:55)

## Slide 14
From ：Mollersten, Biomass and Bioenergy 25(2003)273-285
CO2 absoption
and sequestration by photosynthesis
Regular CCS:
Biomass combustion
Followed by
Limited site, capacity and stability
Energy supply
Charcoal
storage
Unlimited site,
Capacity
Fusion Power Associates 40th annual meeting 2019
BECCS:biomass +CCS for CO2 isolation

## Slide 15
Sustainable world with fusion-biomass
熱
biomass
(CxHyOz)n
heat
heat
Desalination of
Sea water
irrigation
charcoal
Woody biomass
farm
forests
Bio-fuels
Electricity
In future grid
Fusion plant
waste
waste：
FC
PV
gasification
CO2
absorption
Carbon sequestration
Atmosphere CO2
Capture and reduction
Grid parity
Electricity
And
stabilization
Restoration of
Environment,
Forest and
farmland
Returning the carbon from air to coal mines.
Fusion Power Associates 40th annual meeting 2019
Notes: 以上のセルロース、リグニンの吸熱分解実験の結果を用いて、産業廃棄物である木くずの年間排出量596万トンを処理することを目的に、熱交換型反応器の概要設計を行いました。木くずはセルロース７０％、リグニン３０％でなるものとしました。
設計時に用いるガス化パラメータとして、吸熱量と反応時間がありますが、これらについて本研究のデータを用いました。
コチラの図は、実験で得られたパラメータをもとに必要な物質収支、熱供給量、反応時間を満たすように設計した装置の概念です。
バイオマスは細かく粉砕して反応器上部より投入し、水蒸気も同じ流路を上から下に流通します。
一方、伝熱管に反応器下部から上部へと熱媒体を向流で流し、バイオマスへと熱伝達を行い、ガス化を行います。高温ガス炉、または高温の核融合炉を想定して熱媒体はヘリウムと仮定し、伝熱管材料はSiC複合材としました。
こちらが反応器断面の一部になります。このように内径１７ｍｍ、外径２０ｍｍの伝熱管が密に配置され全長は１０ｍ、総本数は29500本となっています。反応熱による吸熱量が大きいために設計上は熱供給が一番厳しい条件になりました。

## Slide 16: Blanket neutronics
>> Monte Carlo neutron transport code, MCNP-5.14
>> FENDL-2.1
>> Toroidal (y-axis) – 48 cm
>> Poloidal (z-axis)– 166 cm
>> 1st wall（F82H・SiC）
>> coolants（water・He）
>> natural LiPb +Be, enriched LiPb
Investigated a possibility of LiPb without enrichment.
→Armor・first wall・configuration of modules are considered・
Fusion Power Associates 40th annual meeting 2019
Notes: ここからはArmor材・第一壁材料・モジュール間ギャップ・冷却領域・ブランケット側壁・増殖材種類まで考慮し、
多様なパラメータがトリチウム生成に与える影響を明らかにするため、具体化されたブランケットデザインを用いて核解析を行いました。
主な比較パラメータは第一壁の種類・冷却材の種類・増殖材の種類となります。

## Slide 17
y
z
PE
Entron
Source
Borate water
PE
PE
C
LiPb
Neutron IP
Boronized PE
x
y
Pb
source
3He detector
neutronics experiment
blanket assembly and small neutron source for transport measurement for actual measurement of tritium self sufficiency
PE
NS
PE
鉛
鉛
鉛
1×109
1×108
2×107
3×106
4×105
PE
Fusion Power Associates 40th annual meeting 2019

## Slide 18
FCs
Oil
Turbine
FT plant case, PCD is supplied by 100 mills/kWh
  Fusion electricity by fuel cells
Cost analysis of energy plant
Fusion Power Associates 40th annual meeting 2019
  For smaller reactor, Fuel cell is more efficient

## Slide 19
ＥＭＰ
T
T
Dump tank
T
T
T
Gas
Chromato-graph
hygrometer
cooler
heater
GC
T
Primary loop
Secondary loop
Expansion
tank
P
F
F
P
MSB
Zr
GC
T
T
economizer
heater
９００℃
９００℃
７００℃
７００℃
～200℃
SiC tube
IHX
module
Test vessel
T
Test section1
Test section2
Test section3
High temperature heat exchanger made of ceramics desired.
Hydrogen production needs special isolation between
primary and secondary coolants.
→IHX transfers heat but prevent
tritium permeation between
primary LiPb or He and secondary.
Energy utilization study
.
SiC compact IHX test model
10kw heat exchanger demonstrated with PbLi/He at 1000 ℃
LiPb-SiC heat exchanger development
Fusion Power Associates 40th annual meeting 2019
Notes: The model of Japan is outlined in the flowing.
Nuclear fusion plant in Japan will be located in coastal area, but NORMTRI assumes that nuclear fusion plant is located in the inland area. In addition, Japanese food culture is different from European food culture. Principal food of Japan is rice but in Europe it is wheat or potato.
So, the sea section was brought into NORMTRI to consider effect of the sea. And, rice compartment was added because rice grows in rice paddy which is covered with water unlike normal agricultural field.

## Slide 20
Tritium extraction from LiPb by vacuum sieve tray is developed.
Fusion Power Associates 40th annual meeting 2019
Extraction of tritium from liquid metal

## Slide 21
Electric Motor
Specimen
Electric Furnace
Mo Support bar
Thermocouple
Mo Crucible
Liquid LiPb or Na
Mo Support bar guide
Mo TC protection tube
Material compatibility assessment
LiPb/SiC/RAFM Compatibility study
Fusion Power Associates 40th annual meeting 2019

## Slide 22: Modelling of Fuel System for self sufficiency
Plasma/VV
Np
Breeding
Blanket
Nbk
Fuel clean up
Nex
Fueling & Storage
Nfu
Isotope separation system
Nis
(tis=1800s)
(tfu=1200s)
(tfs=1800s)
(tp=20s)
(tbk=1.73 × 105)
[D-T]
[D-D]×0.5
[D-T]×TBRDT
[D-D]×TBRDD
Decay & Leak
Decay & Leak
Decay & Leak
Decay & Leak
Dead inventory
Dead inventory
Dead inventory
Dead inventory
Return from 2ndary loops
Exchange Reaction,
Accumulate and saturate
Accumulate continuously,
(Same as decay)
Decay & Leak
Decay
Decay
Decay
Decay
（described with Stella）
Fusion Power Associates 40th annual meeting 2019

## Slide 23
Kyoto Fusioneering assists fusion challengers through
engineering solutions for the energy demonstration.
We provide not only device or design, but integrated consultation to assist efficient power demonstration.
Through the development, transfer of skills and experience from senior to young generation is intended.
Open Innovation by the combination of various industry and research facilities (some reused) are expected.
Kyoto Fusioneering proposes fusion technology options
responding to future energy/environmental needs.
Conclusion
Fusion Power Associates 40th annual meeting 2019