## Slide 1
Suk Jae YOO
Fusion Power Associates,
40th Annual Meeting and Symposium,
December 3rd , 2019/Washington DC, USA
Perspectives and Planning on Fusion Energy Development in Korea
On behalf of National Fusion Research Institute and Korea Fusion Research Groups

## Slide 2
Contents …….
Korea Fusion R&D Program
K-DEMO Strategies
Approach via Virtual DEMO
KSTAR role for Virtual DEMO Approach
Summary

## Slide 3
Daejeon
Gunsan
Plasma Technology Research Center
K-DEMO
ITER**
* Korean Superconducting Tokamak Advanced Research
** International Thermonuclear Experimental Research
Plasma Technology
and Applications
KSTAR*
Nuclear Fusion
and Plasma science
Jeju
National Fusion Research Institute (NFRI)
Seoul

## Slide 4: Basic Plan of Korea Fusion Energy R&D
Phase
Policy Goal
Basic Directions
Basic Promotion Plan
Primary
Strategy for Plan 3
Policy Goal for Plan 3
Establishment of foundation for fusion engineering technology development for demonstrating electricity production
Acceleration for development of DEMO core technology
Strengthening of basic research in fusion and manpower fostering system
Broadening the base of support for fusion energy development
Phase 1 (’07~’11)
Phase 2 (’12~’26)
Phase 3 (’27~’41)
Establishment of a foundation
for fusion energy development
Development of Core Technology for DEMO
Acquirement of construction capability of fusion power plants
Acquisition of operating technology for the KSTAR
Participation in the international joint construction of ITER
Establishment of a system for the development of fusion reactor engineering technology
High-performance plasma operation in KSTAR for preparations for the ITER Operation
Completion of ITER and acquisition of core technology
Development of core technology for the design of DEMO
DEMO design, construction, and demonstration of electricity production
Undertaking of a key role in ITER operations
Completion of reactor core and system design of the fusion power reactor
Commercialization of fusion technology
Basic Promotion Plan 1 (’07~‘11)
Basic promotion plan 5 (‘27~‘31)
Basic promotion plan 6 (‘32~‘36)
Basic promotion plan 7 (‘37~‘41)
Basic promotion plan 3 (‘17~‘21)
Basic promotion plan 4 (‘22~‘26)
Basic promotion plan 2 (‘12~‘16)
Fusion Energy Development Promotion Law (Dec. 2006)
Basic plan for the development and promotion of fusion energy (Aug. 2007)

## Slide 5: A Roadmap toward K-DEMO
ITER
KSTAR
Fusion Technology R&D
Basic R&D
DEMO
Fusion Technology R&D 2
Fusion Technology R&D 1
D-T
Burning

## Slide 6: K-DEMO Design: A Basic Concept
Main Parameters
  R = 6.8 m / a = 2.1 m
  B0 = 7.0~7.4 T / B-peak = 16 T
  elongation = 1.8
  triangularity = 0.625
  Plasma current > 12 MA
  Te > 20 keV
Other Feature
  Double-null & Single-null configuration
  Vertical Maintenance
  Total H&CD Power = 80~120 MW
  P-fusion = 2200~3000 MW
  P-net > 400 MWe at Stage II
  Number of Coils : 16 TF, 8 CS, 12 PF
Demonstrate both electricity generation and commercial feasibility

## Slide 7: K-DEMO Strategies
Strategy 1: Direct K-DEMO Approach
- Demonstrate both electricity generation and commercial feasibility
- Totally new engineering design of K-DEMO
- Net electricity generation > 400 MWe
Strategy 2: Virtual DEMO Approach
- Demonstrate performance of K-DEMO design virtually
- The construction of demonstration reactor is left to the market forces
- KSTAR and ITER will be used as a test bed for K-DEMO design
⇒ Would be a great burden of national program with budget and engineering
⇒ Need to pursue Fusion Reactor Engineering Test Facility as a priority

## Slide 8: Virtual DEMO: Bridges the present (KSTAR, ITER) and the future (K-DEMO)
  Validated simulations with data provided by KSTAR, ITER and Blanket facilities
  Integrated simulations of engineering components (Blanket, BOP, licensing etc)
  Optimization of K-DEMO simulations, Reduced risks and construction costs
K-DEMO
Basic Fusion R&D Program
ITER
KSTAR
Virtual DEMO
High Performance
Plasma Data
Burning Plasma Data
Licensing, System integration
Tritium
Heat exchange
Materials
Optimization
Reduced costs
Blanket R&D Facility

## Slide 9
  Virtual DEMO validation can be made well based on KSTAR, ITER data
  ☞ Simulations validated with KSTAR, ITER experiments
  Decreased uncertainties with high fidelity and accuracy of simulations
  ☞ Reduced risks and construction costs by validated simulations
Devices, Operations
Fusion
Performance
ITER
KSTAR
Virtual KSTAR
Virtual ITER
Validation
Virtual DEMO
K-DEMO
Predictions,
Design,
Validation
V. KSTAR extended through V. ITER up to Virtual DEMO

## Slide 10
V-Tokamak
Resources
1 phase (‘20 ~ ’25)
Virtual KSTAR
~ 1.0 petaflops
HP CPU clusters
4 phase (‘36 ~ ‘40)
V-DEMO Validation
K-DEMO Design
Licensing supports
~ Exascale
HP CPU clusters, GPUs
3 phase (’31 ~ ‘35)
V-Tokamak &
V-BBS
V-DEMO
~ 50.0 petaflops
HP CPU clusters, GPUs
2 phase (‘26 ~ ’30)
Virtual ITER
~ 5.0 petaflops
HP CPU clusters, GPUs
Fusion plasma simulations
Burning plasma simulation validations
Burning plasma simulations
V-BBS
Integrated system design codes development
Blanket simulations development
V-DEMO
Blanket simulations validations
Integrated simulators development and engineering code management
Virtual DEMO R&D Roadmap
V-DEMO incorporates both physical and engineering components of fusion power plants
  V-Tokamak is focused on predictions and uncertainty reduction of fusion reaction physics
  V-BBS integrates Blanket and BOP simulations for engineering designs

## Slide 11
  Large-scale high precision simulation development
  Peta-flops Super-parallel supercomputing techniques
  Efficient simulations with reduced models
  Data analysis and validation with big data techniques
KSTAR
Supercomputer
Validation
Exploration
Virtual KSTAR is the First Step toward Virtual DEMO
Precision simulation for quantitative predictive capabilities
Quantitative validation owing to reliable data of the real KSTAR

## Slide 12: KSTAR has unique hardware advantages for high validation capabilities of virtual tokamaks
▶ SC magnet technology
Lowest error field (𝛿B/B0~1x10-5)
Lowest toroidal ripple (~0.01 %)
▶ ITER relevant In-vessel coils
Uniquely top/middle/bottom coils
Reliable ELM-crash suppression
▶ steady-state heating & CD
Long pulse NBI and ECCD
2nd NBI system is under construction
▶ Advanced diagnostic systems
Profile and 2D imaging diagnostics
Domestic and int’l collaborations
2500 ms (w/ ITB)
4500 ms (w/o ITB H-mode)
6500 ms (w/o ITB L-mode)
#16498
q
psi_n
ECEI
Image bolometer
MSE

## Slide 13
  Progressive achievement of H-Mode long-pulse operation
  ☞ up to 300 s
  Reliable operation for development of new high performance modes
  ☞ Efficient exploration of unknown modes by simulation predictions
  High quality imaging diagnostics
  ☞ Simulation validation and numerical model development
Plasma turbulence observations by imaging techniques
Plasma turbulence simulations with supercomputers
K-DEMO scenario development by KSTAR
KSTAR has been well developed in operation for
exploration of new operation modes

## Slide 14
90
80
(sec)
‘18
(Year)
(Sustaining time)
300 s (2025)
20 s (2013) → 48 s (2014) → 70 s (2016) → 90 s (2018)
  H-Mode long-pulse operation in KSTAR

## Slide 15
▶ Advanced operation modes
    • Internal transport barrier (ITB) > 7 s
    • High beta operation (P > 3.0) > 3 s
ITB mode
Experiments of advanced operation modes by KSTAR
# 18726
# 6123
▶ Active ELM suppression
2011
2017
High beta in 2017

## Slide 16: Upgrade plan of KSTAR for higher beta and steady-state operation
Long-pulse H-mode research
Long pulse H-mode (>70s)
ELM research & control (>30s)
Alternative operation modes (ITB, low q, ..)
Advanced scenario & MHD research
Stable high beta operation
(N >3.0, Tion ~ 10 keV)
Advanced mode develop.
(hybrid, ITB, low q)
MHD & disruption control
Steady-state & reactor mode research
Tungsten divertor & active cooling
Advanced current drive under test
(HFS LHCD & Helicon CD)
Steady-state operation (~300s)
2008
First plasma
(ECH 84 GHz)
Long-pulse H-mode
(NBI~5.5 MW)
(ECH~1 MW)
2017
Heating upgrade
(NBI~12 MW)
(ECH~6 MW)
2021
2021
Divertor upgrade
(Tungsten divertor)
(Detached divertor)
(Diagnostics)
Advanced current drive
(LHCD~4 MW)
(Helicon CD~4 MW)
2025 ~
2017

## Slide 17: Fusion Neutron Irradiation Data
Neutron
Irradiation
Facility
Tritium
Breeding
Tritium
Fuel Cycle
Neutron
Energy
Conversion
Structure
Material
⇒ We are considering various types of fusion neutron sources such as beam-target
sources, volumetric ones, and even a new fission experimental reactor
The Fusion Neutron Irradiation Data are crucial toward the virtual DEMO together with the data of KSTAR and ITER

## Slide 18: Summary
We are going to take a virtual DEMO into consideration for planning the K-DEMO
The virtual DEMO will be much more helpful to optimize the engineering design with uncertainties reduced and accelerate the construction of K-DEMO.
A virtual KSTAR will be the first step toward the virtual DEMO
We will be able to make a good benchmarking of the virtual KSTAR by using the real KSTAR and explore new operating modes of the real KSTAR by using virtual KSTAR, vice versa.
The virtual KSTAR can be easily and reliably extended to a virtual ITER by using the data of the ITER operations.
And then the virtual ITER can also be easily and reliably extended to a virtual DEMO with the experimental data of breeding blankets.
Fusion Engineering Test Facility equipped with a high flux fusion neutron source is crucial for the experimental data of breeding blankets,
We are now making a planning of the fusion engineering test facility with considering several types of fusion neutron sources.

## Slide 19
Around 2035, owing to the success of ITER burning, I hope the recovery of
the honor of fusion energy that has been teased with “the Boy Who Cried Wolf” of Aesop’s Fables
http://pesstevensone.blogspot.com/2013/08/the-boy-who-cried-wolf.html
Thank you for your attention !

## Slide 20: KSTAR (Korea superconducting Tokamak Advanced Research)
Main body
Height: ca. 10 m
Diameter: ca. 10 m
Parameters | Designed | Achieved (~2017)
Major radius, R0 Minor radius, a Elongation,  Triangularity,  Plasma shape Plasma current, IP Toroidal field, B0 H-mode duration N Superconductor Heating /CD PFC | 1.8 m 0.5 m 2.0 0.8 DN, SN 2.0 MA 3.5 T 300 s 5.0 Nb3Sn, NbTi ~ 28 MW C, W | 1.8 m 0.5 m 2.15 0.8 DN, SN 1.0 MA 3.5 T 73 s 4.3 Nb3Sn, NbTi ~ 10 MW C, W