## Slide 1
Focused Energy
Pravesh Patel
Chief Technology Officer
Fusion Power Assoicates Meeting
Washington, DC
December 19, 2023

## Slide 2
Notes: Focused Energy was founded 2 years ago. We’re based in the U.S. and Germany
We’ve rapidly grown to a team of 50 people with core expertise in inertial fusion science, laser technology, and targetry
We’re developing partnerships with national labs, universities, and industry to build a national and international consortium to develop and commercialize IFE

## Slide 3
IFE Science
Building on ICF and NIF ignition—exploring advanced schemes to achieve high gain and robust performance
Laser Technology
Mature driver technology—diode-pumped solid-state lasers (DPSSL)
Target Technology
Target fabrication technologies scalable to mass production and automation

## Slide 4
In ICF we need to compress and heat DT fuel to high density and high temperature
Hydro-instablity stress on target quality
Symmetry stress on laser & target
Low fuel mass limited gain
M. Tabak et al., Phys. Plasmas 1, 1626 (1994)
Fast Ignition
hot
spot
High r with a low velocity implosion
High T with a separate heating source
fuel
Hydro-stability relaxed target quality
Asymmetric relaxed laser requirements
High fuel mass high gain
Central Hotspot Ignition
hot
spot
High r &T simulataneously
High velocity, high convergence implosion
fuel
Fast Ignition has the potential for high gain and robustness

## Slide 5
In the 2000’s it was discovered that short-pulse lasers could generate intense beams of protons
High-intensity laser
Highly collimated, high energy, short-pulse proton beam
R. Snavely, et al, PRL, 85, 14, 2945 (2000); P. K. Patel, et al, PRL, 91, 125004 (2003); M. Roth et al., PRL 86, 436 (2001)
Electrostatic sheath field
50µm
Distance
Time
10-100’s eV
temperatures

## Slide 6
Proton Fast Ignition
Shell
Coated CH
Ablation layer
Seals, protects fuel
DT wetted foam
Low density CH foam supporting 3 mg DT
Hemispherical foil
Metallic foil with hydrogen-rich layer
Focuses protons
Cone
Protects foil
Guides protons
Long-pulse lasers
Spherically illuminate shell, compressing DT fuel to high density
Short-pulse lasers
Accelerate protons from hemispherical foil

## Slide 7
Our current designs indicate that we can achieve target gains >100 with 2 MJ laser energy
Solid DT 363 µm
DT gas
1341 µm
EL = 1.7 MJ (2w)
mDT = 2.7 mg
vimp = 200 km/s
rmax = 400 g/cm3
rR = 2.8 g/cm2
1D design
Temperature
Density
Proton energy dep
2D core heating simulations
0
0.5
1.5
1
2.5
2
3
0
25
50
75
100
125
150
Gain
Laser Energy (MJ)
Fusion gain
PFI (ideal)
NIF (2023)

## Slide 8
Laser Technology: we have already developed and deployed the technology for our first kJ-class laser system
2 kJ @ shot/min beamline
operational at ELI Beamlines
Large aperture liquid-cooled amplifier technology
We are designing a 1 kJ, 10 Hz laser that will be the unit building block of an IFE FPP

## Slide 9
Target Technology: we’re developing fabrication methods for low cost, mass manufacturing of IFE targets
Fabrication techniques for capsule shell, foam, and cone that scale to 10 Hz mass manufacturing
15,000 sq.ft. facility operational in 2024

## Slide 10
The key for both science & technology risk-reduction is a sub-scale, high rep-rate IFE implosion facility
1/3 spatial scale (1/30 energy scale) of FPP
48 LP + 8 SP beams (60 kJ total energy)
Dedicated IFE facility with spherically symmetric illumination geometry, capable of studying both direct-drive central hot spot and fast ignition schemes

## Slide 11
The key for both science & technology risk-reduction is a sub-scale, high rep-rate IFE implosion facility
Phase I
Flashlamp-pumed lasers (shot/3 min)
DT wetted foam targets
Capability for 100+ shots/day giving very high data return for experimental optimization of parameter space
Requires significant level of automization (target production, delivery, and alignment, laser alignment and operations, data acquisition and processing)

## Slide 12
The key for both science & technology risk-reduction is a sub-scale, high rep-rate IFE implosion facility
Phase II
Install diode-pumped beamlines (10 Hz)
Add target injection and tracking capability for 10 Hz operation
Upgrade diagnostics to 10 Hz operation
Fully integrated systems testing (at sub-scale) of laser, targetry, control systems, and implosion performance at 10 Hz operation

## Slide 13
This facility will provide the technical basis and confidence to then scale up to a high-gain FPP
1750 kJ LP + 250 kJ SP
G>100, 10 Hz
50 kJ LP + 10 kJ SP
shot/3 min, 10 Hz
3x spatial
30x energy

## Slide 14
Pravesh Patel
CTO, Focused Energy
pravesh.patel@focused-energy.world
Notes: We