## Slide 1
December 2-3, 2024 | FPA | Washington, D.C.
Cary Forest | CSO
cary@realtafusion.com

## Slide 2: We are advancing the axisymmetric magnetic mirror fusion concept
HTS planar magnets Bm ~25 T
Axial difference in magnetic field generates mirror force to confine charged particles
B0
Confinement improves with higher mirror ratio
C.B. Forest | Realta Fusion | FPA

## Slide 3
Rm=2
Breakeven
Brief History of US Mirror Confinement up to 1986
Lawson Diagram
2XIIB
1976
2XIIB 1976
beta =1 , 10 keV
MFTF
BB1
1969
MFTF
1986
MFTF-B Tandem
TMX-U
1982
Tandem Confinement

## Slide 4: New advances in technology, computational capability and physics understanding are reinvigorating the magnetic mirror fusion concept
HTS
~ 2x field possible from previous technology
Advanced Stabilization
Axisymmetric mirrors possible
Advanced heating systems
Modern NBI, ECH, and ICRH systems.
17 T WHAM Coil
NBI Source
RF Energization
C.B. Forest | Realta Fusion | FPA
Notes: Find more attractive advanced stabilization photo eventually

## Slide 5: Realta Fusion’s FPP* roadmap
Experiment: WHAM
De-risk technology & validate physics
CFS-built HTS magnets
NBI, ECH, ICRH
Commercialization:
Hammir (FPP)
Axisymmetric tandem magnetic mirror
Fully integrated net-energy generator demonstration
Prototype: Anvil
  Demonstrate long pulse plasma at HAMMiR End-Plug conditions and fusion power plant nuclear technology at scale
  Can be optimized for DT neutron yield for a VNS-like device
* FPP = Fusion Pilot Plant
D. Endrizzi et al., “Physics basis for the Wisconsin HTS Axisymmetric Mirror (WHAM),” Journal of Plasma Physics, vol. 89, no. 5, p. 975890501, 2023. https://doi.org/10.1017/S0022377823000806
C. B. Forest et al., “Prospects for a high-field, compact break-even axisymmetric mirror (BEAM) and applications,” Journal of Plasma Physics, vol. 90, no. 1, p. 975900101, 2024. https://doi.org/10.1017/S0022377823001290
C.B. Forest | Realta Fusion | FPA
Notes: Cary
First version of Beam 100 keV NBI ; HAMMiR endplug would use RF and approach MeV energies

## Slide 6: Hammir makes use of Anvil end plugs to construct an axisymmetric tandem mirror configuration for FPP
D.A. Sutherland | Realta Fusion | EPRI Fusion Forum
End Plugs
Strongly Driven By RF, NBI, Non-Maxwellian Plasma
4x planar ~ 25 T HTS magnets
Full-scale demonstrate with ANVIL simple axisymmetric mirror
Central Cell
Maxwellian plasma with high-gain fusion plasma conditions, low-field magnets, scalable in length to change power output
Notes: Cary
First version of Beam 100 keV NBI ; HAMMiR endplug would use RF and approach MeV energies
HAMMiR – High-Field Axisymmetric Magnetic Mirror Reactor

## Slide 7
$10M ARPA-E funded project, WHAM
(Wisconsin HTS Axisymmetric Mirror)
October 2020
Spin-out company established
September 2022
June 2024
Seed round led by Khosla Ventures
U.S. Dept. of Energy Milestone contract
Commercial energy production
Decarbonizing heavy industry
mid 2030s
2029
Anvil: proof at scale
(volumetric neutron source)
May 2023
May 2024
Develops RealTwinTM
plasma simulator
(hosted on AWS)
World-record breaking first WHAM plasma: 17 Tesla
July 2024
timeline

## Slide 8: Revisit the classical simple mirror with higher mirror ratio and high field magnets using modern modeling
Classical Mirror confinement
For NBI fueled plasma
For DT Fusion
Fusion gain is independent of size or B
Egedal, J., Endrizzi, D., Forest, C. B. & Fowler, T. K. Fusion by beam ions in a low collisionality, high mirror ratio magnetic mirror. Nucl Fusion 62, 126053 (2022).

## Slide 9: What sets minimum size for a beam-heated breakeven-class experiment at RM=10?
Interchange/ballooning beta limit sets density:
neutral beam shine through sets plasma radius:
Kinetic Stability (DCLC) sets normalized plasma size:
FLR stabilization sets plasma length:
Unique solution from 1-3:
Eb | 100 keV
beta | 0.3
B0 | 3 T
a0 | 0.3 m
n20 | 0.9
L | 4 m
Nrho | 25
Pnbi | 7 MW
J. Plasma Phys. (2024), vol. 90, 975900101, 2024.
Published by Cambridge University Press
doi:10.1017/S0022377823001290
Prospects for a high-field, compact break-even
axisymmetric mirror (BEAM) and applications
C.B. Forest 1, J.K. Anderson1, D. Endrizzi 2, J. Egedal 1, S. Frank 2,
K. Furlong2, M. Ialovega1, J. Kirch1, R.W. Harvey3, B. Lindley1,
Yu.V. Petrov3, J. Pizzo1, T. Qian 4, K. Sanwalka1, O. Schmitz1, J.Wallace1, D. Yakovlev1 and M. Yu1,†

## Slide 10: Compact, high field mirror leads to attractive Tandem Mirror Designs
axisymmetric classical tandem mirror
(no thermal barriers)
Submitted to J. Plasma Phys. (2024)
Published by Cambridge University Press
arXiv preprint ar.Xiv:2411.06644. 2024 Nov 11.
Integrated modelling of equilibrium and transport in axisymmetric magnetic mirror fusion devices
S. J. Frank, J. Viola, Yu. V. Petrov, J. K. Anderson, D. Bindl, B. Biswas, J. Caneses, D. Endrizzi, K. Furlong, R. W. Harvey, C. M. Jacobson, B. Lindley, E. Marriott, O. Schmitz, K. Shih, C. B. Forest
Tandem Mirror POPCON
A new simpler way to obtain high fusion power gain in tandem mirrors, Fowler, T. K., Moir, R. W. & Simonen, T. C.. Nucl Fusion 57, 056014 (2017).
C.B. Forest | Realta Fusion | FPA

## Slide 11: Scaling the simple and tandem axisymmetric mirror to high performance plasma conditions
MFTF-B Tandem
TMX-U
1982
Tandem Confinement
HAMMiR
ANVIL
WHAM
2XIIB
1976
MFTF
1986
C.B. Forest | Realta Fusion | FPA

## Slide 12
WHAM is newly operational and addressing MHD stability and mirror confinement

## Slide 13
C.B. Forest | Realta Fusion | FPA
Phased WHAM Project Approach
  WHAM is a $20M machine built on $10M budget.
  State-of-the-art HTS mirror coils + a lot of surplus equipment
System | Phase 1 (2024) | Phase 2 (2025)
Mirror coils | 17.05 T | 17.05 T
End-ring biasing (stability) | 2 MW bipolar waveforms | 
NBI | ~24 kV, <800 kW, 20 msec | 
RF: fast wave |  | 4 – 30 MHz, < 1 MW
ECH | 110 GHz, <600 kW, 20 msec | 
Vacuum | <2,000 L/s turbos / cryos | >100,000 L/s Ti, Ta gettering
Central field | < 0.3 T, R ~ 50 – 70 | 0.3 – 0.9 T, R = 20-50

## Slide 14
Diverse Sourcing of Components on WHAM
  Archimedes transmitter via
System | Phase 1 2024 | Phase 2 2025
Mirror coils | 17.05 T | 17.05 T
End-ring biasing (stability) | 2 MW bipolar waveforms | 
NBI | ~24 kV, <800 kW, 20 msec | 
RF: fast wave |  | 4 – 30 MHz, < 1 MW
ECH | 110 GHz, <600 kW, 20 msec | 
Vacuum | <2,000 L/s turbos / cryos | >100,000 L/s Ti, Ta gettering
Central field | < 0.3 T, R ~ 50 – 70 | 0.3 – 0.9 T, R = 20-50
C.B. Forest | Realta Fusion | FPA

## Slide 15: Results from the first experimental campaign on WHAM
Cary Forest, Jay K. Anderson1, Oscar Anderson1, Ted Biewer3, Dominick Bindl2, Bodhi Biswas2, Mike Brown4, Mike Clark1, Elliot Claveau2, Jan Egedal1, Doug Endrizzi2, Sam Frank2, Kiesuke Fujii3, Kieran Furlong2, Mykola Ialovega1, Jeremiah Kirch1, Grant Kristofek5, Spencer Kwan1, Xavier Navarro-Gonzalez1, Ben Lindley2, Ed Marriott2, Vladimir Mirnov1, Bob Mumgaard5, Solomon Murdock1, Everett Penne1, Jon Pizzo1, Steve Oliva1, Tony Qian1, Kunal Sanwalka1, Oliver Schmitz1, Kai Shih2, Mary Severson1, Benjamin Terranova1, Aaron Tran1, Jesse Viola2, John Wallace1, Dmitry Yakovlev1, Mason Yu1
1 University of Wisconsin-Madison
2 Realta Fusion
3 Oak Ridge National Lab
4 Swarthmore College
5 Commonwealth Fusion Systems
66th APS DPP 10/11/24
WHAM plasma 7/15/24
Photo credit: Mason Yu

## Slide 16: CFS delivers HTS magnets
Specifications – NINT magnet design operates continuously in DC mode with conduction cooling (liquid cryogen-free)
mass: 1500 kg height: 2.1 m width: 1.2 m
bore diameter: 55 mm bore length: 310 mm length
axial load limit: 63 tons
Record field (MCF) – 17 T on axis (on plasma)
Continuous operation – 1st campaign upon commissioning lasted 82 days and maintained full field for 78 days, both magnets landed safely at end of campaign
Turnkey magnets – CFS delivered a complete package of self-contained systems with all necessary functions to operate magnets “out of the box”, each including:
Low infrastructure – operation only requires electrical power, cooling water, data
Fast installation – installed on day 1, pumping down on day 2, cooling on day 3, and first plasma 2 weeks after delivery
Performance Parameter [unit] | Design target | Measured performance
Field on axis [T] | 17 | 17.05
Peak field on winding pack [T] | 20 | *
Stored Energy (per magnet) [MJ] | 3.2 | *
Engineering current density [A/mm2] | 178 | *
Operating temperature (1st stage) [K] | 60 | 47.7
Operating temperature (2nd stage) [K] | 20 | 11.0
Operating current [A] | 2000 | 1727
Winding pack power (at full current) [W] | * | 1.1
Estimated heat load to 1st stage [W] | 180 | 167
Winding pack
  Cryostat
  Power supply
  Cryogenics
  Vacuum system
  Instrumentation & Controls
  Operational and monitoring software
  All customer facilities interfaces
Above: Dual magnet qualification testing at CFS-1, Devens, MA
* Parameter not predicted or measurable

## Slide 17
Flux loops
Foil bolometers
Key diagnostics for equilibrium, fluctuations
Fast visible camera
mm wave
319 GHz Interferometer
Z=0, single-chord
Flux Loop 1
Z = 7.8 cm
R = 25 cm
Flux Loop 2
Z = 33.0 cm
R = 20 cm
Flux Loop 3
Z = 52.2 cm
R = 15 cm
Travelling Limiter
R = 3.425 cm
Z = (69.8, 78.8) cm
Edge Fluctuation Ring
Z = 57.1 cm
R = 5.7 cm
4T 110 GHz
ECH Resonance
Fast ion turning point
Rm=2, 1.72 T, 13.6 MHz
ICRF Resonance
11-chord Ion doppler spectrometer
20-chord AXUV photodiode
Z=0
NBI Shine-Through array
11+4 chord Secondary Emission Detectors
Phantom Fast Camera
40-150k frames per second
ECH Split-Waveguide
4T 110 GHz
ECH Resonance
Adjustable Mirror

## Slide 18: WHAM research mission derisks MHD instabilities, probes microstability
9
Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2024 |  |  |  |  |  |  |  |  |  |  |  | 2025 |  |  |  |  |  |  |  |  |  |  |  | 2026 |  |  |  |  |  |  |  |  |  |  | 
Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
>100
plasma shots/day
commissioning
early MHD
advanced MHD
MHD and performance exploration
Step 2:
limit neutrals CX to confine fast ions from NBI. Expect FLR stabilization of high m at modest fast ion concentration.
Step 3:
Suppress low m MHD instabilities via biasing or other techniques.
Step 4:
Performance extension
Achieve collisionless regime
Explore mstability limits of loss-cone ion distribution
Study effect of rf
  Ponderomotive stabilization
  Enhanced plugging
Step 1:
Observe, identify, probe MHD instabilities.
Rapid iteration with,
validation of,
RealTwinTM models
construction

## Slide 19
Typical WHAM discharge: bulk + fast pressure
Reliable breakdown with 30 - 400 kW ECH into ~.05 m3 plasma
Line-averaged densities of 0.03 – 5 x 1019 m-3
Distinct dual population: warm plasma + hot electrons
  Warm bulk decay < 1 msec.
    Collisional; majority of density
  Hot e- slow pressure, minority density decay on much longer timescale
    Majority of pressure
nwT + nfe <Ee>
nfe <Ee>
0
10
20
30
40
50
Time (ms)
2.0
1.0
0
1019
200
100
0
300

## Slide 20
NBI fueling accesses high density regime
NBI into dense target plasma adds fueling
Fast ion confinement in Phase 1 limited by charge exchange losses, per expectations.
Warm plasma timescale increases modestly relative to ECH-only
0
5
10
15
20
25
30
Time (ms)

## Slide 21
V
Ring Bias
Gaining control of MHD: Imposed rotation
Mirror plasma natural rotates in ion diamagnetic direction.
Positive bias enhances flow;
Negative bias opposes and can reverse flow
    NP12.00145 Qian

## Slide 22
Rotating plasma reduces fluctuations, stores more energy
0
2
4
6
8
10
12
Time (ms)
    NP12.00145 Qian

## Slide 23
Summary
  WHAM is operational.
  ECH breakdown creates reliable target plasma with controlled density.
  Expected MHD signatures observed (high- and low- m).
  Imposed rotation affects and reduces fluctuations.
  Hot electrons are well confined, > 1 second beyond ECH pulse.

## Slide 24: Aiming for a DT fusion fuel cycle for Anvil and first Hammir FPP design point - potential use of Anvil as VNS
Blanket / fuel cycle technology needs for Anvil and Hammir:
  Flowing liquid metal blankets (e.g., PbLi) / molten salt (e.g., FLiBe) mostly parallel to magnetic field (axially)
  Radiation tolerant first wall materials (i.e., first RAFM, advanced alloys later)
  Tritium processing / handling systems needed for any DT-based FPP
Opportunity to optimize Anvil for DT fusion neutron production and use as VNS for testing materials and test blanket modules
  Sub-gain long-pulse to steady-state operation (Q ~ 0.1-1) at ~1-10 MW-class fusion power output
  Relatively low-cost access to > 1 MW/m2 DT neutron wall loadings over large volumes, enabling parallel testing of materials / blanket modules
  Reach high-dpa in materials in a reasonable amount of time with DT neutrons.
  Evaluating other fuel cycle design points that may eliminate need for breeding blanket for VNS
C. B. Forest et al., “Prospects for a high-field, compact break-even axisymmetric mirror (BEAM) and applications,” Journal of Plasma Physics, vol. 90, no. 1, p. 975900101, 2024. https://doi.org/10.1017/S0022377823001290
C.B. Forest | Realta Fusion | FPA

## Slide 25
Axisymmetric simple mirror with HTS magnets
  Q ~ 1 device is near-term economical source of DT neutrons and reactor-relevant heat flux which enables evaluation of tritium breeding blankets, tritium fuel cycle elements, materials damage, plasma material interactions, and large bore HTS magnets
Physics advantages
  No disruptions (no net current)
  Stabilization techniques identified
  Compact (HTS enabled)
  Intrinsically steady-state (no pulsed power)
Engineering advantages
  Manufacturability (simple linear design)
  Upgradeability (length, radius, heating)
  Modularity and flexibility (expander cells, TBMs, test coupons)
Operational advantages
  Inspectability (linear design facilitates access)
  Maintainability (modularity enabled)
  Reliability
  Availability
BEAM (now Anvil) could be FIRST—integrated DT blanket testing at ~1-10 MW scale
C.B. Forest | Realta Fusion | FPA

## Slide 26: Science and Technology Gaps Addressed by Anvil as FIRST
Tritium Breeding Blankets
  Tritium breeding ratio, nuclear heating, flow of conductive fluids in high magnetic fields
  Modular design to simultaneously evaluate designs using liquid metals, molten salts, ceramics
Tritium Fuel Cycle
  Tritium self-sufficiency, steady-state, closed fuel cycle
  Direct internal recycling, impurity removal, isotopic separation systems, detritiation systems
  Accountancy, safety, licensing
Materials Degradation
  High DT neutron flux
  Large volume available for testing
  High magnetic field, high temperature
Plasma Material Interactions
  First wall material evaluations
  High heat flux, DT neutron flux, tritium, alphas
High Field Magnets
  Large-bore HTS magnets and cables
  Compact fusion concept
  High neutron flux
APS-DPP Community Planning Process, "A Community Plan for Fusion Energy and Discovery Plasma Sciences," 2020.
NASEM Final Report of the Committee on a Strategic Plan for U.S. Burning Plasma Research, 2019.
C.B. Forest | Realta Fusion | FPA

## Slide 27: Advanced heating systems are required to advance magnetic mirror towards high performance plasma conditions
Likely heating technology needs for ANVIL & HAMMIR:
  Steady-state ECH ~ 3-6 MW @ 170 GHz
  Steady-state ICRH ~ 5-10 MW @ 50-200 MHz
  Steady-state negative ion beam NBI w/ ~ 10-40 MW @ 100-500 keV beam energy
NBI neutralization efficiency for positive and negative ion beams
R.S. Hemsworth and T. Inoue, IEEE Trans. Plasma Sci. 33(6), 1799 (2005).
Image source: iter.org, https://www.iter.org/node/20687/japan-develops-first-high-output-multi-frequency-gyrotron
Ongoing full wave RF simulations
C.B. Forest | Realta Fusion | FPA