## Slide 1: The EUROfusion approach to DEMO and fusion energy
Ambrogio Fasoli
Programme Manager

## Slide 2: About EUROfusion
EUROfusion integrates R&D in fusion science and technology
29 Countries
31 Research Institutions
164 Universities
~1000 MSc & PhD students
~5000 Fusion Researchers & Support Staff

## Slide 3: R&D program follows the European Fusion Roadmap
Current resource allocation
Short-term
Medium-term
Long-term
Milestone
Lower cost through concept improvements and innovations
Stellarator as fusion plant?
Material research facilities IFMIF/DONES
DEMO
Consistent
concept
Commence
construction
Electricity
production
ITER
First plasma
Full performance
Research on present and planned facilities, analysis and modelling
Fusion Power Plants

## Slide 4: Main elements of the Roadmap revision
Definition of the DEMO step
Gaps to be addressed
Measures to accelerate the DEMO and FPP (fusion power plant) programmes
These points are in addition and in synergy with the activities for ITER, which remain central

## Slide 5: Definition of the DEMO step – high level goals
Demonstrate performance and integration of key technologies with tolerable failure rates to achieve adequate levels of availability
  Self-sufficient fuel cycle
  Robust plasma operation scenario & power-exhaust
  Intrinsic safety and tolerable impact of waste
  Phase 1: blanket radiation exposure 20dpa (~7y)
  Phase 2: net electricity output ~300MW (tpulse~hours)
  Tokamak configuration
Notes: Why 20dpa ? He content still very low (200-300 appm) and database from specimen irradiated in fission material test reactors is relevant

## Slide 6: Example of system code exploration of DEMO low aspect ratio solution
Requirements
τburn ≥ 2h
Pel,net ≥ 350 MW
Constraints
≤ 6 MW.T/m
EU-DEMO ‘24 | 
 | 2.8
[m] | 8.6
Pfus [MW] | 1651
[MWe] | 350
() | 3.6 (3.3)
[hr] | 2.11
[T] | 4.39
EU-DEMO ‘24 | 
 | 2.8
 | 8.6
Pfus [MW] | 1651
 | 350
 | 3.6 (3.3)
 | 2.11
 | 4.39
Notes: The proposed design point fulfills the stakeholder requirements with margin in exhaust and lower TF
incorporating plasma uncertainties (+/-50%) into the design allows to lower the targeted fusion power
q95 increase provides operational safety for the plasma scenario (less disruption prone at higher q95).
the heat flux in case of reattachment has almost been halved, now in the window for mitigation

## Slide 7: Gaps to be addressed
Notes: + theory and numerical simulations

## Slide 8: Breeding Blanket in DEMO: main reference concepts
Water Cooled Lead Lithium (WCLL)
Breeder/neutron multiplier: PbLi (6Li at 90%) liquid (~330°C)
Coolant: Water (295-328°C)
T extraction from recirculating PbLi
Helium Cooled Pebble Bed (HCPB)
Breeder: Li4SiO4 + Li2TiO3 in form of a pebble bed, 6Li at 60%
Neutron multiplier: Beryllide (TiBe12) rods
Coolant: He 300-520°C @ 8 MPa
T extraction with purge Helium
P. Arena et al, (2023) Design and Integration of the EU-DEMO Water-Cooled Lead Lithium Breeding Blanket, Energies, 16, 2069
G. Zhou et al, (2023) The European DEMO Helium Cooled Pebble Bed Breeding Blanket: Design Status at the Conclusion of the Pre-Concept Design Phase, Energies, 16, 5377

## Slide 9: Breeding Blanket in DEMO: improved variants
Water Cooled Lead Lithium Concept (WCLL) – Double Bundle
Breeder zone and first wall in series (Tin,FW ≈ 315 °C)
Less tubes, less welds, less surface, less water, more PbLi
 more reliable, lower T permeation, better TBR
 avoids PbLi - water interaction
Water-cooled Lead and Ceramic Breeder (WLCB)
Neutron multiplier: molten Pb or solid Pb compound
Coolant: Water (285-325°C @15.5 MPa)
T extraction with purge Helium: 0.1% H2/H2O@ ~0.2 MPa
Breeder zone and first wall in series (Tin,FW ≈ 315 °C)
Available TER and water PWR technology
Good TBR and neutron shielding, low T permeation
P. Pereslavtsev et al, (2023) Neutronic Activity for Development of the Promising Alternative Water-Cooled DEMO Concepts, Appl. Sci., 13, 7383,

## Slide 10: Materials
A development programme is needed to qualify materials to enable roll-out of FPPs
  response to plasma exposure and to 14-MeV n-irradiation >20dpa
  mechanical and thermal properties
  chemical compatibility and safety issues
Robustness of industrial fabrication must be increased
IFMIF-DONES will be the only facility with neutrons of adequate spectrum and fluence to qualify materials

## Slide 11: IFMIF-DONES: construction has started
At Escúzar, Granada, Spain
Operation expected in ~2034
Pictures taken on Oct 16, 2024

## Slide 12: DEMO Phase 1 or a Volumetric Neutron Source ?
While burning plasma physics require large fusion power (~500 MW in ITER), nuclear technology tests require low fusion power (~50 MW), but need high n-fluence (>10 dpa)
The combination of high power for physics testing and high fluence for nuclear technology testing in a single device leads to high T consumption
The feasibility of a Volumetric Neutron Source (VNS) to qualify components is under consideration (instead of, or as a different version of, DEMO Phase 1)
Physics basis
  14 MeV neutron source with peak Neutron Wall Loading ≥ 0.5 MW/m2
  Beam-target reactions (like JET) to keep machine size low
  NBI also employed to drive Ip, as there is no space for large CS
  bN < 3.5; max. B-field on TF ~ 13T (LTS, but HTS options are also explored)
  q95 > 3; R ≤ 3m and Pfus < 50MW

## Slide 13: Present view of the VNS design – comparison to ITER
 | VNS | ITER
Linear Size, Ro, (m) | 2.5 | 6.2
Fusion power (MW) | <50 | 500
Plasma current (MA) | 1.7 | 15
Magnetic Field (%) | 5.4 | 5.3
Q | <1 | 10
Beams energy (keV) | 120 | 1000
Beams power (MW) | 45 | 33
ECH (MW) | 10 | > 40
Plasma volume (m3) | 23 | 1300
Plasma surface (m2) | 80 | 900
Power consumption (MW) | 170 | 
Neutron wall (MW/m2) | 0.5 | 1
Fluence (dpa) | 50 | 0.3

## Slide 14: The VNS as an element of the DEMO plant ?
DEMO_2
DEMO_1 / VNS
Active Maintenance Facility
Electrical system
Balance of Plant
T, Fuelling, Vacuum
Cooling systems
Cryo
DEMO Assembly hall
DEMO_1 / VNS Assembly hall

## Slide 15: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Strong synergy with new ITER Baseline (W-related work)
exploitation of JT-60SA
(integrated in our Tokamak Exploitation programme)

## Slide 16: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
  Digitalization effort, including innovative AI approaches

## Slide 17: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site

## Slide 18: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site
Development and maintenance of adequate workforce
  Connections with academic and industrial networks, diversity at all levels

## Slide 19: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site
Development and maintenance of adequate workforce
Mutually beneficial new international collaborations
  Collaborations with China (CRAFT, EAST, BEST, …), US (SPARC, …) etc., for technology facilities and early burning plasma developments

## Slide 20: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site
Development and maintenance of adequate workforce
Mutually beneficial new international collaborations
Knowledge management
  Document lessons learned in the ITER design and developments

## Slide 21: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site
Development and maintenance of adequate workforce
Mutually beneficial new international collaborations
Knowledge management
Parallelization of activities to reduce sequential ITER-DEMO coupling

## Slide 22: Measures to accelerate the DEMO program
Strengthening R&D in the identified gap areas
Increased effort in simulations for plasma and for engineering
Streamlining licensing for fusion and rapidly identifying site
Development and maintenance of adequate workforce
Mutually beneficial new international collaborations
Knowledge management
Parallelization of activities to reduce sequential ITER-DEMO coupling
Public Private Partnerships and involvement of industry

## Slide 23: Measures to accelerate the Fusion Power Plant program beyond DEMO
Dedicated test facilities to qualify technologies for FPPs that will be different from DEMO
Increase attractiveness of FPPs
  Stellarator FPP design studies
  HTS and advanced magnet assembly
  Advanced structural materials
Source: ITER
Source: IPP

## Slide 24
Notes: Design & construction of ITER will inform design & construction of DEMO
Operation of ITER will inform operation of DEMO (not design)

## Slide 25
Thank You!