## Slide 1
  Presented by Max Karasik on behalf of
The Laser Plasma Branch,
Plasma Physics Division
US Naval Research Laboratory
DISTRIBUTION STATEMENT A. Approved for public release: distribution unlimited.
An outlook on laser fusion: Focusing on science and enabling future progress
FUSION POWER ASS0CIATES 44th Annual Meeting
December 20th, 2023, Washington DC
Work supported by US DoE/NNSA

## Slide 2: NRL program advances fundamental NNSA science and is developing a promising path for high-yield ICF applicable to IFE
Conducts a vibrant program that includes experiments, theory, simulation, and workforce development
    Flexible facility capable of focused experiments, diagnostic development, and code validation
    Balanced approach of external collaboration and internal research goals
    Unique capabilities – short wavelength, ISI smoothing, bandwidth, zooming, diagnostics
As a federal employees, NRL laser-fusion program provides an independent voice in the field
NRL is the world-leading center for high energy excimer lasers
    Offers a path to a future high-yield ICF/IFE facility using a sub-megajoule driver
    Enabled by superior target physics with ArF laser and modern implosion designs
    Transformational: robust 10’s-100’s MJ yields with sub-MJ laser system capable of shot-on-demand

## Slide 3: What is unique about NRL’s excimer laser-target facility and what is it good for?
World’s highest uniformity and deepest ultraviolet multi-kilojoule laser-target facility
Premier facility for doing focused hydrodynamic experiments
  High pressure drive without contamination from hard x-rays or hot electrons
  Drive uniformity without the complexity of a hohlraum
  Advanced diagnostics: Monochromatic x-ray imaging, advanced spectroscopy, 1D and 2D VISAR; 5th harmonic probing
Uniquely suited for investigating multi-beam LPI with broad bandwidth
Mid-scale facility with hands-on operation excellent for workforce development

## Slide 4: State-of-the art diagnostics and highly uniform drive make the facility extremely well suited for focused experiments with broad ICF/IFE applications
Pioneering study of isolated defects present in all ICF implosions
Zulick, C et al., PRL, 125, 055001 (2020).
Zulick, C et al., PoP, 27, 72706 (2020).
Velikovich, AL et al., PoP, 27, 102706 (2020).
Foams are useful for HEDP and IFE, but challenging to model accurately
Advanced x-ray imaging and uniform drive allow unique platform for shock propagation and EOS measurement of these materials
Y. Aglitskiy et al., PoP 25, 032705
Experimental vs. tabulated Hugoniot for 10% solid density CH foam
Compressibility measurement on Nike 10% solid density CH foam

## Slide 5: NRL has collaborations on high impact efforts across the complex
X-ray radiograph
at NRL
LANL 3D printed foam lattice
with LANL on structured foams
with LLE on Imprint mitigation using burn-through membrane
400 Å Pd
37337
uncoated
26494
400 Å Au coating
uncoated
Development on NIKE
Implementation on Omega
NIF PDD implosions

## Slide 6: NRL is participating in the IFE hubs
Inertial Fusion Science and Technology hub
Colorado State University (leader)
Cornell University
General Atomics
Los Alamos National Laboratory
Marvel Fusion
SLAC National Accelerator Laboratory
Texas A&M University
U.S. Naval Research Laboratory
University of Illinois Urbana-Champaign
Xcimer Energy Corp.
DOE release: https://www.energy.gov/articles/doe-announces-42-million-inertial-fusion-energy-hubs
The 3 hubs are:
Inertial Fusion Energy-Consortium on Laser-Plasma Interaction Research hub
Inertial Fusion Science and Technology hub
National Science and Technology Accelerated Research for Fusion Innovation & Reactor Engineering hub
CSU link https://engr.source.colostate.edu/csu-to-lead-doe-funded-multi-institution-hub-to-advance-laser-driven-fusion-energy/

## Slide 7: Achievement of ignition at NIF is a milestone for all fusion research
Results of decades of work – need to exploit investment for near-term (3-5 yrs.)
At the time of the decision to build NIF, new approaches for direct drive
ICF were nascent and not sufficiently developed for full scale facility
What is the best path to high yield capabilities (10’s-100’s MJ)? (>5 yrs.)
Sufficient progress in direct drive ICF has been achieved to deserve serious consideration for the next generation high-yield facility
Laser gain ~ 1.5x
Capsule gain > 10x
Shot N221205
(3.15 megajoules)
2022
Fusion Yield (MJ)
Laser gain ~ 0.7x
Capsule gain ~ 5.7x
(1.35 MJ/230 kJ)
> 3 MJ yield has been achieved with ~ ¼ MJ energy absorbed by the pellet

## Slide 8: Direct drive couples ~4x more energy into the imploding shell giving higher yields for a given laser energy
But details matter – direct drive still must overcome problems
Coupling of laser to pellet
Uniform illumination
Mitigate laser-plasma instabilities
N210808
1.9 MJ
Laser
N210808
1.35 MJ
Yield
230 kJ
N210808
Direct drive eliminates major energy losses for indirect drive
Shot N210808 capsule gain ~5.7x @ 230 kJ
Substantially less than 1 MJ of energy ignites the NIF pellet
10-20% of
Laser Energy
Drives Capsule
Excimers are an attractive laser driver for high performance ICF*
Shorter laser wavelength to further suppress LPI and increase hydro-efficiency of implosion
Highly uniform target illumination
Multi-THz bandwidth to suppress LPI
Capable of zooming the focal diameter to follow imploding target
The 193 nm ArF laser best meets all of the above criteria
*See JASON report (2021)

## Slide 9: Broad bandwidth and short wavelength will enable robust ICF and IFE
Basic Research Needs Report (BRN 2023) identifies short wavelength, broad bandwidth drivers as enabling technology for IFE
Broad bandwidth 3ω (351 nm) lasers for direct drive proposed by U of Rochester Laboratory for Laser Energetics (LLE) (D. Turnbull, et al., APS/DPP 2023)
Argon Fluoride (ArF) laser driver offers 10 THz bandwidth with the crucial benefit of short wavelength (193nm) and high efficiency
The high drive pressure enabled by short wavelength and wide bandwidth opens up the parameter space
NNSA Applications
Inertial Fusion Energy
More robust, higher gain implosions => high yield with smaller driver

## Slide 10: High yields (10’s-100’s MJ) are possible in conventional direct drive designs using sub-MJ of ArF laser light with focal zooming - even higher yields with shock ignition
High yields at < 1 MJ laser energy with two different designs indicate robust physics
Increased coupling and higher drive pressure with short wavelength gives higher yield
Low-aspect ratio shell:
Robust against hydro instability
A. J. Schmitt, PoP 30, 012702 (2023)

## Slide 11: Sub-MJ ArF laser and shock ignition maintain high yield in 2D simulations
includes effects of laser imprint and target surface roughness
Higher drive pressure allowed by ArF -> lower aspect ratio -> more stable implosions
A. J.Schmitt, PoP 30, 012702 (2023)
Time
0.6 mm
0.12 mm
temperature
density
Aspect ratio 3.7 pellet, ArF shock ignition: 61 MJ yield with 411 kJ of laser energy

## Slide 12: With broadband & deep UV ArF laser, higher LPI thresholds and high absorption allow target to be driven at higher pressure
Cross-Beam Energy Transport
(CBET)
Absolute Two-Plasmon Decay Instability
(TPD)
Absolute TPD threshold for 6 ArF beams in an Omega-scale plasma is about 5.5x higher than the 3w Nd:glass laser with currently realizable bandwidths (~1 THz)
Absolute SRS-backscatter instability threshold for ArF beams exceed those of 3w Nd:glass laser for NIF-like plasma conditions
Absolute Stimulated Raman Back Scattering
(SRS)
Simulations by J. Bates using LPSE code
in collaboration with LLE scientists
J. W. Bates, PoP 30, 052703 (2023)

## Slide 13: The world’s leading expertise and capability in short wavelength, broad bandwidth drivers is at NRL
NRL is the only lab with the short wavelength, high bandwidth approach for NNSA applications
World-leading capability in excimer lasers developed over decades thanks to NRL’s unique nexus of pulsed power, laser and plasma physics expertise
Leading expertise in direct drive physics and robust implosion designs
Deep UV excimer laser technology at the kJ level demonstrated at NRL
Clear development path has been developed to the ~30 kJ level driver module
With the short wavelength and broad bandwidth, direct drive high gain (~100) implosions require less than a MJ driver energy

## Slide 14: Key excimer technologies demonstrated at NRL (Leverages ONR, FES, and ARPA-E funded programs)
90,000 laser shots (10 hrs) continuous @ 2.5 Hz
300,000 laser shots in 8 days of operation
World record ArF energy (200 J)
Electra laser facility
Demonstrated ~100k shot capability (KrF)
Zooming demonstrated on Nike
Focal Zooming
Increases laser coupling and mitigates CBET
11 THz ArF bandwidth
0.3% beam uniformity on Nike
single pass
ASE output
D. Kehne, RSI, 84, 013509 (2013)
A. Deniz, Opt. Commun. 147, 402 (1998)
J. D. Sethian, IEEE Trans. Plas. Sci., 38, 4 (2010)

## Slide 15: Path forward to robust high-yield facility takes advantage of laser drive modularity
.
Excimer beamline
20-30 kJ on target
full shock ignition intensity and large plasma - LPI at scale
Simulations & theory
3D hydro-implosions
Improved LPI mitigation
Implosion physics
Gain sufficient for ICF
λ=193 nm vs 351 nm
22 modules x 30 kJ = 660 kJ
High Yield Implosion Facility
NIKE is a prototype of large scale excimer lasers
Facility could be sited elsewhere (DoE labs, industry partners)
Designs and smaller tests would come from NRL - technologies would be transferred to partner laboratories
Modularity of system can be exploited – build from 10’s MJ up to 100’s MJ

## Slide 16: NRL program advances fundamental NNSA science and is developing a promising path for high-yield ICF applicable to IFE
Conducts a vibrant program that includes experiments, theory, simulation, and workforce development
    Flexible facility capable of focused experiments, diagnostic development, and code validation
    Balanced approach of external collaboration and internal research goals
    Unique capabilities – short wavelength, ISI smoothing, bandwidth, zooming, diagnostics
As a federal employees, NRL laser-fusion program provides an independent voice in the field
NRL is the world-leading center for high energy excimer lasers
    Offers a path to a future high-yield ICF/IFE facility using a sub-megajoule driver
    Enabled by superior target physics with ArF laser and modern implosion designs
    Transformational: robust 10’s-100’s MJ yields with sub-MJ laser system capable of shot-on-demand